## Slide 1
DIGITAL LOGIC & COMPUTER ARCHITECTURE PROJECT
4-Bit Binary Arithmetic Calculator
Using Logisim Evolution
TEAM MEMBERS
P. Surya — 2620030573
K. Vedesh — 2620030383
V. Praveen — 2620030643
V. Nikhilesh — 2620030443
0011 + 0010 = 0101
01 / 06

## Slide 2
02 — INTRODUCTION & OBJECTIVES
Why Computers Think in 0s and 1s
Binary numbers use only two digits: 0 and 1. Computers use them because electronic switches have two clear states — OFF (0) and ON (1). Our 4-bit calculator takes two 4-bit numbers and performs addition and subtraction using only logic gates.
OBJECTIVES
Understand binary numbers and arithmetic
Learn how basic logic gates work
Design a 4-bit adder-subtractor circuit
Build and test it in Logisim Evolution
INPUT → PROCESS → OUTPUT
Input A
(4-bit)
Input B
(4-bit)
Arithmetic Circuit
(Add / Subtract)
Result
(4-bit)
Carry
(1-bit)
Two 4-bit numbers enter, the circuit computes, and a 4-bit result plus carry comes out.
02 / 06

## Slide 3
03 — THEORY & LOGIC CIRCUIT
Gates → Half Adder → Full Adder
AND: output 1 only if all inputs are 1
OR: output 1 if any input is 1
NOT: flips the input (0→1, 1→0)
XOR: output 1 if inputs differ
Subtraction uses two's complement: A − B = A + (NOT B) + 1. Inverting B and adding 1 lets the same adder subtract.
HALF ADDER
A
B
Sum
Carry
Sum = A ⊕ B
Carry = A · B
FULL ADDER = 2 HALF ADDERS + OR
A
B
Cin
HA 1
A⊕B
HA 2
Sum
Cout
Sum = A ⊕ B ⊕ Cin
Cout = A·B + Cin·(A ⊕ B)
Half adder adds two bits, giving Sum and Carry
Full adder adds A, B and an incoming carry (Cin)
HA1 carry and HA2 carry are ORed to form Cout
Chaining full adders adds multi-bit numbers
03 / 06

## Slide 4
04 — CIRCUIT DESIGN IN LOGISIM EVOLUTION
4-Bit Adder-Subtractor Schematic
HOW CONTROL M WORKS
M = 0: B ⊕ 0 = B and C0 = 0, so the circuit adds A + B
M = 1: B ⊕ 1 = NOT B and C0 = 1, so it computes A + NOT B + 1 = A − B (two's complement)
ADD / SUBTRACT CONTROL
M
XOR on B bits
+ Carry-in C0
0 → Add | 1 → Subtract
04 / 06
M
Add/Sub
C0 = M
A3
B3
FA3
S3
Cout
A2
B2
FA2
S2
C3
A1
B1
FA1
S1
C2
A0
B0
FA0
S0
C1
Result[3:0] = S3 S2 S1 S0 • Carry ripples FA0 → FA3 → Cout • Yellow gates = XOR (Bi ⊕ M)

## Slide 5
05 — SIMULATION RESULTS & TRUTH TABLE
Expected Results, Ready to Verify
Input A Op Input B Result Decimal
0011 + 0010 0101 3+2=5
0101 + 0011 1000 5+3=8
0110 − 0010 0100 6−2=4
1000 − 0011 0101 8−3=5
Example: 0110 − 0010 → 0110 + 1101 + 1 = 1 0100. The 4-bit result is 0100; the final carry of 1 is discarded.
A B Cin Sum Cout
0 0 0 0 0
0 0 1 1 0
0 1 0 1 0
0 1 1 0 1
1 0 0 1 0
1 0 1 0 1
1 1 0 0 1
1 1 1 1 1
Insert actual Logisim Evolution simulation screenshot here
These are the mathematically expected outputs. Every result must be verified by running the implemented circuit in Logisim Evolution before final submission.
05 / 06

## Slide 6
07 — CASE STUDY
Case Study: Applying the 4-Bit Binary Arithmetic Calculator
BUILT & TESTED IN LOGISIM EVOLUTION
Placed 4 full adders and 4 XOR gates on the canvas
Wired inputs A, B and the SUB control pin
Tested sample values with pins and LEDs
Checked each result against a truth table
PURPOSE & BENEFITS
See binary math happen gate by gate
Safe, free, hands-on circuit practice
Builds the foundation for ALU and CPU design
LOGISIM CIRCUIT — SIGNAL FLOW
Input A
A3 A2 A1 A0
Input B
B3 B2 B1 B0
SUB control
0 = add • 1 = sub
4 × XOR
B ⊕ SUB
4 Full Adders
Ripple carry
Cin = SUB
Sum Output
S3 S2 S1 S0
Carry Out
Cout / overflow
Cin = SUB
[ Insert Logisim Evolution screenshot here ]
Show circuit running a sample, e.g. 0110 + 0011 = 1001
SAMPLE TESTS
SUB=0: 0110 + 0011 = 1001 (6+3=9)
SUB=1: 0111 − 0010 = 0101 (7−2=5)
07 / 07

## Slide 7
06 — CONCLUSION & APPLICATIONS
From Gates to the Heart of a CPU
Built a 4-bit adder-subtractor from four full adders and XOR gates
Learned how AND, OR and XOR gates combine to add and subtract binary numbers
Used two's complement so one circuit handles both operations
APPLICATIONS
CPUs • ALUs • Calculators • Embedded Systems • Microcontrollers
FUTURE WORK
Add AND, OR and XOR operations with an operation selector to create a simple ALU.
CPU
Control Unit
Registers
ALU
Adder / Subtractor
Memory
Our circuit lives inside the ALU
Thank You
Questions welcome • 1010 1011
06 / 06