## Slide 1
0101
COMPUTER ORGANIZATION & DIGITAL DESIGN
4-Bit Binary Arithmetic Calculator
FIRST-YEAR ENGINEERING PROJECT

## Slide 2
MODULE 1 · 02
Introduction & Objectives
A digital circuit that adds, subtracts and compares two 4-bit numbers. Computers store everything as binary digits — 0 (low voltage) and 1 (high voltage).
Input: two 4-bit operands A, B + operation select
Processing: logic gates & adders compute the result
Output: 4-bit result + carry / overflow flags
OBJECTIVES & RELEVANCE
Build an ALU from basic logic gates
Understand how CPUs perform arithmetic
Foundation for processors, calculators & embedded chips
A = 0101
B = 0011
Calculator Circuit (ALU)
Result = 1000
INPUT → PROCESS → OUTPUT

## Slide 3
MODULE 1 · 03
Number Systems & Logic Gates
1010₂ = 10₁₀ = A₁₆
Binary (base 2): 1·8 + 0·4 + 1·2 + 0·1 = 10
Decimal (base 10): everyday counting
Hexadecimal (base 16): 0–9, A–F; one hex digit = 4 bits
BASIC LOGIC GATES
AND: 1 only if all inputs are 1
OR: 1 if any input is 1
NOT: inverts the input
NAND / NOR: inverted AND / OR
XOR: 1 if inputs differ · XNOR: 1 if inputs match
NAND IS UNIVERSAL
A B │ A NAND B │ A NAND A
0 0 │ 1 │ 1
0 1 │ 1 │ 1
1 0 │ 1 │ 0
1 1 │ 0 │ 0
A NAND A = NOT A — so NAND can build NOT, AND and OR.
A
B

## Slide 4
MODULE 2 · 04
Combinational Logic & Arithmetic Circuits
Half adder: Sum = A ⊕ B, Carry = A·B
Full adder: adds A, B and carry-in Cin
Ripple-carry: 4 full adders chained, each carry feeds the next
Subtraction: A − B = A + (NOT B) + 1 (two's complement)
FA3 FA2 FA1 FA0
Carry ripples ← from FA0 to FA3. Cout = final carry-out.
WORKED EXAMPLE (5 + 3 = 8)
0101₂
+ 0011₂
= 1000₂
Carry-out = 0 → unsigned result 8 is correct
Signed overflow = 1: +5 + +3 gives 1000 = −8, beyond the +7 limit
Overflow occurs when two same-sign inputs give an opposite-sign result
Subtract: 0101 − 0011 = 0101 + 1101 = 0010 (2)

## Slide 5
MODULE 2 · 05
Designing the 4-Bit ALU
ADD: A + B
SUB: A − B (two's complement)
AND / OR / XOR: bitwise logic on each bit pair
SLT: result = 0001 if A < B (signed), else 0000
MULTIPLEXER & CONTROL
All units compute in parallel. A 3-bit operation-select signal drives a multiplexer that passes only the chosen result to the output (e.g. 000 = ADD, 001 = SUB, 010 = AND, 011 = OR, 100 = XOR, 101 = SLT).
A[3:0]
B[3:0]
ALU
Result[3:0]
Cout · V
Op Select [2:0]

## Slide 6
MODULE 3 · 06
Sequential Logic & Registers
Combinational: output depends only on current inputs — no memory (adders, ALU, MUX).
Sequential: output depends on inputs AND stored state — has memory (flip-flops, registers).
D flip-flop: copies D to Q on the rising clock edge
Clock: timing signal that synchronizes updates
Reset: clears stored value to 0000
Result is held until the next clock-enabled calculation or reset
Counters & FSMs sequence steps — the basis of processor control
4-BIT RESULT REGISTER
1 0 0 0
Q3 Q2 Q1 Q0
CLK ⎍⎍⎍⎍ · RST → 0000

## Slide 7
MODULE 4 · 07
Register File & Memory
Reg A
Reg B
ALU
Reg Result
Operands are read from registers, processed by the ALU, and the result is written back on the clock edge.
Register file: small, fast set of registers selected by number
RAM: read/write memory — each address holds stored data
ROM: read-only memory, e.g. fixed programs or lookup tables
Address selects a location; data is the value stored there
IMPLEMENTED
Registers A, B and Result built from D flip-flops inside the calculator.
OPTIONAL EXTENSION
RAM to save past results; ROM to store preset test operations.

## Slide 8
MODULE 5 · 08
Connection to the RISC-V Processor
Stored-program: instructions and data live in memory
ISA: the instruction set a CPU understands
Fetch → Decode → Execute, repeated each cycle
ADD → add rd, rs1, rs2
SUB → sub rd, rs1, rs2
AND → and rd, rs1, rs2
OR → or rd, rs1, rs2
SLT → slt rd, rs1, rs2
Our ALU is a building block of a CPU — not a full RISC-V processor.
PC
Instruction Memory
Register File
ALU
Control Unit
SIMPLIFIED SINGLE-CYCLE DATAPATH
Control decodes the instruction and sets the ALU operation-select — the same signal our calculator uses.

## Slide 9
MODULE 6 · 09
Implementation, Testing & Extensions
Inputs A,B → 4-bit ALU → LED Display → Result Reg*
Op-select switches drive the ALU · *result storage is optional
# OP A B EXPECTED
1 ADD 0101 0011 1000
2 SUB 0111 0010 0101
3 AND 1100 1010 1000
4 OR 1100 1010 1110
5 XOR 1100 1010 0110
6 SLT 0010 0101 0001
SIMULATION TOOLS
Built and verified in Logisim Evolution or Digital — switches for inputs, LEDs for outputs, step-by-step clock.
OPTIONAL EXTENSIONS
More operations: NOR, shift left/right
Wider ALU: 8-bit or 16-bit operands
Memory-mapped LED output
Zero and negative status flags

## Slide 10
MODULE 6 · 10
Conclusion & Future Scope
Logic gates → adders → a complete 4-bit ALU
Registers and control signals link it to CPU architecture
Same ALU concept powers RISC-V cores and embedded systems
Future: 8-bit ALU, shifter, FSM control, FPGA build
REFERENCES
M. Morris Mano — Digital Design
Harris & Harris — Digital Design and Computer Architecture: RISC-V Edition
Patterson & Hennessy — Computer Organization and Design: RISC-V Edition
Logisim Evolution documentation
1111
Thank You
Questions welcome